## Slide 1: FIRI Simulator - PyFIInS
John Lightfoot (UKATC)
Colm Bracken (NUI Maynooth)
Roser Juanola-Parramon (UCL, NASA Goddard)
Gibion Makiwa (U.Lethbridge)

## Slide 2
Requirements
Public code
Free, portable, no special hardware  Python
Able to model the ‘strawman’ design.
  2 flux collectors with 2m primary mirrors
  Tethered with baselines up to 80m
Flexible – design / observing mode / target
Able to observe any target
Able to model physics and systematic effects

## Slide 3
Design: User Interface
Excel ‘instrument; file describing instrument configuration / observation timeline
FITS format ‘target’ file with object to ‘observe’ – github CUBEFORMAT.com

## Slide 4
User Interface – the instrument file
FTSpectrograph

## Slide 5
User Interface – the instrument file
Interferometer

## Slide 6
User Interface – the instrument file
Telescope

## Slide 7
User Interface – the instrument file
Background

## Slide 8
User Interface – the target file
FITS format described in CUBEFORMAT.md
Target ‘toolkit’:
  Spectrum generation
    T, β, peak flux, lines and features
      Forsterite
      Protostar
      Comet
  Image generation
    From FITS
    ‘ring’, ‘thick disk’, ‘comet’
  Spectrum + image = cube
  Cube1 + cube2 +… = target_cube
  T Tauri disk

## Slide 9
The Calculation
Efficiency:
  numpy and scipy for array calculations
  Parallel Python (www.parallelpython.com) for parallelization
    8GB laptop good for Band4 25-50cm-1 (R = 50)
    64GB desktop for Band2 100-200cm-1 (R = 100)
Process:
  PyFIInS target cube  interferograms
  PyDataProcessing interferograms  dirty cube
Timings:
  Band 4, 4 + 1 hours
  Band 2, 8 + 2 hours

## Slide 10
Physics and Systematic Errors
Physics:
  Thermal noise from instrument elements
  Photon noise from background (CMB, CIB, Zodiacal light)
  Cosmic ray strikes (from SPIRE)
Systematics:
  Primary beams from realistic optics
  Temperature fluctuations
  Collector pointing errors
  Baseline pointing errors
  FTS beam combiner mirror errors (from SPIRE)
  Continuous baseline movement
  Detector time constant

## Slide 11
Results
HTML weblog
Interferograms / dirty cube in FITS format

## Slide 12
Results – PyFIInS weblog 1

## Slide 13
Results – PyFIInS weblog 2

## Slide 14
Results – PyFIInS weblog 3

## Slide 15
Results – PyFIInS weblog 4

## Slide 16
Results – PyFIInS weblog 5

## Slide 17
Results – PyDataProcessing weblog 1

## Slide 18
Results – PyDataProcessing weblog 2

## Slide 19
Results – PyDataProcessing weblog 3

## Slide 20
Results – PyDataProcessing weblog 4

## Slide 21
Installation
Code at www.github.com/handofkwll/fisica
Instructions for Linux/OSX in README.md
‘instrument’ file for strawman instrument - Band 4
‘target’ file with circumstellar ring - Band 4
Cookbook – pre-stellar cores example

## Slide 22
Examples 1 – Prestellar cores

## Slide 23
Examples 2 – Comet

## Slide 24
Examples 3 – T Tauri disk (P. Woitke, St.Andrews)